## Slide 1
Blackhole Tensix Tile — NoC subsystem
Tensix Tile
Compute (5 RISC-V)
BRISC (drives NoC 0)
NCRISC (drives NoC 1)
TRISC 0
TRISC 1
TRISC 2
Local memory
L1 SRAM
1.5 MB
source / target
of every
NoC packet
NIU (Network Interface Unit) — one per NoC ×2 per tile
CMD BUF × 4
0x800 stride
FIFO per buf
Command / Status registers (base = NOC_REGS_START_ADDR + offset)
Address
TARG_LO
0x00
TARG_MID
0x04
TARG_HI
0x08
RET_LO
0x0C
RET_MID
0x10
RET_HI
0x14
Control
NOC_CTRL
0x1C
CMD_CTRL
0x40
PACKET_TAG
0x18
Atomic
AT_LEN_BE
0x20
AT_DATA
0x28
★ Multicast (new in Blackhole)
BRCST_EXCLUDE
0x2C · 24-bit mask
NOC_CTRL command bits
BRCST_PACKET (b5) BRCST_XY (b16) BRCST_SRC_INCLUDE (b17) ★ combined with BRCST_EXCLUDE for per-mcast destination drop
NoC 0 router · X-Y routing
NoC 1 router · Y-X routing (disjoint from NoC 0)
↑ N ↓ S ← W → E 2D mesh links to neighboring Tensix / DRAM / PCIe / ARC tiles
Fig. — BRCST_EXCLUDE is a Blackhole-generation register (absent in Wormhole) that lets a single multicast issue drop a bitmask of destinations inside the target rectangle. HW & firmware expose it; the kernel-facing dataflow API does not yet wire it through.